## Slide 1
EXPERIMENT OVERVIEW
STEMI vs NSTEMI | 1D CNN experiment
Clinical question
Can a 12-lead ECG distinguish STEMI from NSTEMI among patients already diagnosed with acute myocardial infarction?
Open dataset
Du et al. ACS ECG dataset
Figshare article 29925314 v1
CC0 public-domain license
2,618
patients
one ECG per patient
1,420
STEMI
54.2%
1,198
NSTEMI
45.8%
Raw ECG
The CNN reads the 12-lead waveform directly; no clinical fields enter the model.
Scope: subtype classification within an MI cohort. This experiment does not test MI detection in a general population.
Notes: Source: Du et al. ACS ECG dataset, Figshare article 29925314 v1. Experiment implementation and results: https://github.com/Bearior/EKG-MI-TEST

## Slide 2
DATA PIPELINE
Cohort construction and ECG processing
Patient-level split
Split | Total | STEMI | NSTEMI
Train | 1,570 | 852 | 718
Validation | 524 | 284 | 240
Test | 524 | 284 | 240
Signal preparation
1 Median-center each lead
2 Bandpass filter, 0.5 to 40 Hz
3 Resample 500 Hz to 100 Hz
4 Feed 12 × 1000 samples into CNN
Verified ACS data
One ECG / patient
12-lead signal
1D CNN
Held-out test
Notes: The split uses one ECG per patient to avoid patient overlap. Processing settings come from the repository pipeline.

## Slide 3
METHOD
Raw waveform and 1D CNN
Direct 12-lead input
12
ECG leads
10 s
signal per patient
100
samples per second
3
convolution blocks
64
channels in final block
CNN architecture
1D convolution: 16 → 32 → 64 channels
Batch normalization + ReLU + pooling
Global average pooling
One STEMI output score
Training and selection
Adam, learning rate 0.001
15 epochs; batch size 64
Best epoch 14 by validation AUROC 0.837
Threshold 0.512 from validation
Notes: Feature counts and model settings come from the experiment report and saved training artifacts in the repository.

## Slide 4
RESULTS
Held-out test results
Test set
n = 524
Discrimination
AUROC 0.802
Average precision 0.813
Threshold metrics
Balanced accuracy 0.745
Sensitivity 0.761
Specificity 0.729
Precision 0.769
F1 score 0.765
Notes: Evaluation figure generated by the repository pipeline on the untouched test partition. Threshold 0.612 was selected on validation data.

## Slide 5
WHAT WE LEARNED
Interpretation and limitations
CNN confusion matrix at threshold 0.512
Actual class | Predicted NSTEMI | Predicted STEMI
NSTEMI | 175 | 65
STEMI | 68 | 216
The CNN detected 216 of 284 STEMI cases, versus 160 for logistic regression. It also flagged 65 NSTEMI cases as STEMI, versus 35 before.
Limits of this result
Internal hold-out evaluation only
Angiography-selected ACS cohort
Single training seed
No external hospital validation
No calibration study for clinical use
Next experiment
Test the CNN on an external cohort and repeat training across several seeds. Compare sensitivity and specificity at clinically chosen thresholds.
github.com/Bearior/EKG-MI-TEST
Notes: These results support continued model development, not clinical deployment. Repository: https://github.com/Bearior/EKG-MI-TEST